## Slide 1: An Efficient Tracker for Thyroid Nodule Detection and Tracking during Ultrasound Screening
Ting Liu, Xing An, Bin Lin, Yanbo Liu, Wenlong Xu, Yuxi Liu, Longfei Cong, and Lei Zhu()
Shenzhen Mindray Bio-Medical Electronics, Co., Ltd., Shenzhen, China

## Slide 2
Content
1. Background
2. Methods
3. Results
4. Conclusion

## Slide 3
1. Background

## Slide 4: Background Clinical Background
Common in clinic
Incidence rising rapidly throughout the world
Large amounts of ultrasound videos
  time-consuming
  great challenges for doctors
Unclear boundary & similarity between nodules and tissues
  false detection

## Slide 5: Background Challenges
Red: the ground truth
Yellow: nested prediction
Green: normal tissues that are similar to nodules
less attention is paid to ultrasound videos
Nested predictions still remain after post-processing
Misdetection of normal tissues

## Slide 6
2. Methods

## Slide 7: Methods Network Architecture
Inputs:
The current frame
The previous frame
The heatmap generated from objects in the prior frame
Outputs:
The predicted rectangles
The classification probability of each prediction
The center offset of tracked boxes in adjacent frames

## Slide 8: Methods Fusion Module
To better fuse the feature of inputs
Extract the features of each input
Squeeze-and-excitation (SE) block
  learn the importance of each input

## Slide 9: Methods Advanced Post-processing Module
Potential of technology development needs to be harnessed to respond industry challenge

## Slide 10: Methods Advanced Post-processing Module
Potential of technology development needs to be harnessed to respond industry challenge
Selection Function
Classification | Detection boxes | Tracking offsets
: focal loss | : L1 loss : GIoU loss | L1 loss
Classification | Detection boxes | Tracking offsets
Loss Function

## Slide 11: Methods Minibatch Self-supervised Learning Module
the feature vector of the nodule in a batch
obtain the most dissimilar nodule feature vector to
: obtain the most similar normal tissue feature vector to the
Margin: preset similarity threshold
Batch-based similarity loss function

## Slide 12: Methods Experiments
Potential of technology development needs to be harnessed to respond industry challenge
1555 movies, 13,314 images
Annotation
  five doctors & an expert
Nodule size (462 to 232,672 pixels, mean: 29,979 pixels)
  small (<1503 pixels), middle (1503 pixels, 6923 pixels) and large (＞6923 pixels)
Traing set (80%)
  movies: 1244; images: 10597
Validation set (10%)
  movies: 155; images: 1363
Testing set (10%):
  movies: 156; images: 1354

## Slide 13
3. Results

## Slide 14: Results Quantitative Analysis
Method | FPR | Recall | Prec | AP | AP50 | RCLL | MT | ML | Speed
CenterNet | 16.1 | 79.5 | 83.7 | 45.2 | 74.8 | NA | NA | NA | 28fps
YoloSiam | 21.6 | 76.3 | 78.2 | 41.7 | 70.5 | 66.8 | 61.0 | 25.0 | 16fps
CenterTrack | 13.5 | 82.1 | 85.3 | 48.1 | 77.4 | 76.6 | 65.4 | 16.0 | 28fps
Ours | 3.8 | 91.2 | 95.8 | 56.8 | 88.2 | 86.4 | 76.9 | 5.8 | 30fps
Method | FPR | Recall | Prec | AP | AP50 |  |  |  | Speed
CenterNet | 16.1 | 79.5 | 83.7 | 45.2 | 74.8 | NA | NA | NA | 28fps
YoloSiam | 21.6 | 76.3 | 78.2 | 41.7 | 70.5 | 66.8 | 61.0 | 25.0 | 16fps
CenterTrack | 13.5 | 82.1 | 85.3 | 48.1 | 77.4 | 76.6 | 65.4 | 16.0 | 28fps
Ours | 3.8 | 91.2 | 95.8 | 56.8 | 88.2 | 86.4 | 76.9 | 5.8 | 30fps
Table 1. Performance comparison on the thyroid dataset (%).

## Slide 15: Results Quantitative Analysis
Potential of technology development needs to be harnessed to respond industry challenge
Method | FPR | Recall | Prec | AP | AP50 | RCLL | MT | ML
Baseline | 13.5 | 82.1 | 85.3 | 48.1 | 77.4 | 76.6 | 65.4 | 16.0
+F | 12.9 | 83.3 | 85.8 | 48.3 | 78.2 | 78.2 | 67.9 | 14.7
+F+AP | 8.4 | 85.4 | 90.5 | 51.0 | 82.5 | 80.9 | 71.2 | 10.3
+F+AP+MSL | 3.8 | 91.2 | 95.8 | 56.8 | 88.2 | 86.4 | 76.9 | 5.8
Method | FPR | Recall | Prec | AP | AP50 |  |  | 
Baseline | 13.5 | 82.1 | 85.3 | 48.1 | 77.4 | 76.6 | 65.4 | 16.0
+F | 12.9 | 83.3 | 85.8 | 48.3 | 78.2 | 78.2 | 67.9 | 14.7
+F+AP | 8.4 | 85.4 | 90.5 | 51.0 | 82.5 | 80.9 | 71.2 | 10.3
+F+AP+MSL | 3.8 | 91.2 | 95.8 | 56.8 | 88.2 | 86.4 | 76.9 | 5.8
Table 2. Results of ablation studies based on pretrained ResDCN-18 (%)
Method | FPR | Recall | Prec | AP | AP50 | RCLL | MT | ML
Baseline | 14.1 | 81.3 | 85.1 | 46.6 | 75.7 | 76.1 | 63.5 | 17.9
+F | 12.6 | 82.7 | 86.0 | 48.3 | 78.0 | 77.8 | 67.3 | 15.4
+F+AP | 9.8 | 84.9 | 88.9 | 50.7 | 81.2 | 79.8 | 69.2 | 11.5
+F+AP+MSL | 4.9 | 88.5 | 94.6 | 55.2 | 87.5 | 83.8 | 72.4 | 7.7
Method | FPR | Recall | Prec | AP | AP50 |  |  | 
Baseline | 14.1 | 81.3 | 85.1 | 46.6 | 75.7 | 76.1 | 63.5 | 17.9
+F | 12.6 | 82.7 | 86.0 | 48.3 | 78.0 | 77.8 | 67.3 | 15.4
+F+AP | 9.8 | 84.9 | 88.9 | 50.7 | 81.2 | 79.8 | 69.2 | 11.5
+F+AP+MSL | 4.9 | 88.5 | 94.6 | 55.2 | 87.5 | 83.8 | 72.4 | 7.7
Table 3. Results of ablation studies based on DLA-34 (%)

## Slide 16: Results Qualitative Comparison

## Slide 17: Results Qualitative Comparison
frame
frame
frame
frame

## Slide 18: Results Qualitative Comparison
Potential of technology development needs to be harnessed to respond industry challenge
Nodule with unclear boundray
Two nodules on a frame
Big nodule

## Slide 19
4. Conclusion

## Slide 20: Conclusion Conclusion
Potential of technology development needs to be harnessed to respond industry challenge
Fusion module
  combine features of previous and current frames
  acquire better detection and tracking result
Advanced post-processing mechanism
  train the model to select the optimal prediction
  boost the detection accuracy
Minibatch self-supervised learning module
  enhance the ability of distinguishing nodules from similar tissues
  reduce the false positive rate

## Slide 21
THANK YOU
company presentation｜confidential